## Slide 1
Share-governor effect on hydrogen consumption: SDP EMS on FTP-75
Offline walk (tools/ems_walk.py), governor on vs off, plant loss map, fw v27 governor package, λ = 0.41 SoC/g
+0.06 %
ΔSoC-matched (equivalent) hydrogen with the governor, relative to governor-off
Raw H2 −1.16 %, but the pack drains 8.2e-5 more SoC (0.20 mg H2-equivalent). Net effect is zero within resolution.
ems-ftp75-sdp (sdp-v6, 350 s) | H2 [g] | ΔSoC | eq-H2 vs off
Governor off (walk) | 0.016456 | −0.013295 | reference
Governor on, symmetric plant (walk) | 0.016266 | −0.013377 | +0.06 %
Governor on, M2 asymmetry (walk) | 0.016293 | −0.013366 | +0.07 %
Board, fw v27, campaign H | 0.016389 | −0.013340 | anchor
Walk vs board on this leg: H2 −0.59 %, ΔSoC +0.2 %. Campaign repeatability floor 250–800 ppm; a bench A/B with a governor-bypass build could not resolve +0.06 %.
Governor effect across the FTP-75 legs (walk, symmetric plant)
Chart: 
| hold-5050 | soc-band | mpc-sto | sdp-v6 | dp-replay
Raw H2 change [%] | -2.64 | -3 | 18.9 | -1.16 | 0.71
ΔSoC-matched change [%] | -0.04 | -0.33 | 0.19 | 0.06 | 0.02
How to read the number
Model estimate: both arms in the same reduced demand/pack/H2 model; the governor-on arm reproduces the suite's fw v27 walk table on every shared leg.
"Governor" = minority clip, HOLD/feedforward, cuts and load guard, fw v27 battery-only start and k_d schedule. The off arm keeps the fw v26 ceiling bound (inert here: 0 clamped stages).
Why small: no ceiling ever binds and the SDP shares sit inside the minority band; the battery-only start only shifts 0.2 mg onto the pack, which the ΔSoC price returns.
Sign stable over λ 0.409–0.4165 (+0.04 to +0.06 %). Real governor costs elsewhere: ems-sdp-cross +5.0 %, all ftp75c legs −10 to −16 % (battery-only start never releases under the 0.30 A gate).
Notes: Sweep: 24 walkable ems-* legs x 3 arms (off, on symmetric, on M2 asymmetry). Governor-off is the heuristic_walk() anchor. Board anchor: HIL Results/hil_report_20260904_022637/scenario_ems-ftp75-sdp_hifi/analysis.json.